## Slide 1
Motivation
    The segmentation of anatomical structures in volumetric scans is a challenging and time-consuming task.
    Segmentation is hard – low tumor-to-liver contrast (~30 HU), poor quality or resolution.
Input
    CT slices
    Hand motion and gestures acquired by the Leap Motion
3D Anatomy Segmentation using Perceptual Computing
S. Shenzis, M. Samson, R. Vivanti , L. Joskovitz
The Rachel and Selim Benin School of Computer Science and Engineering The Hebrew University of Jerusalem
Email: shlomo.shenzis@mail.huji.ac.il moshe.samson@mail.huji.ac.il
Introduction
Method
    Inaccuracies – segmentation leaks
    Time Consuming interaction
    Tedious task
Results and Validation
Summary
The Problem
Our Solution
    A semi-automatic tool for 3D segmentation in volumetric medical scans using natural input from the user.
Output
    2D – Correct segmentation of the anatomy.
    3D – Mesh of the corrected anatomy.
Algorithm
    Initial Scribble on 2D slices
      Input acquired by natural interaction with the user: hand gestures and finger tracking.
    Segmentation
      Grow-Cut algorithm.
    Correction Scribbles on 3D Mesh
      Annotate lesions versus correct regions on the 3D anatomy mesh.
    Leaks Removal
      3D correction of segmentation lesions using contour smoothness value.
    Repeating stages 1-2, 3-4
      Iteratively repeat stages 1-2 and 3-4, until a satisfying result is obtained.
Experimental Results - quantitative examination
    10 cases from 10 different patients
    Ground truth – Radiologists approved segmentation on CT.
    Comparison metrics:
      DICE volumetric overlap error (VOE)
      Volumetric Similarity (VS)
      Average Hausdorff Distance (AHD)
    Semi-automatic 2D soft-anatomy segmentation using natural input
    Grow-Cut algorithm for 2D segmentation
    Graph-based lesions removal using contour smoothness and gradient as cost function.
    0.8491% of Volumetric Overlap Error
    Segmentation and 3D mesh of the kidney
    Input: CT slices
    Leap Motion Device
 | VOE | VS | AHD
CASES | 0.75579 | 0.89359 | 0.61523
 | 0.90427 | 0.99365 | 0.13195
 | 0.91288 | 0.96977 | 0.22423
 | 0.86508 | 0.89655 | 0.3529
 | 0.84497 | 0.88513 | 0.29112
 | 0.83341 | 0.89295 | 0.38871
 | 0.87731 | 0.90688 | 0.19493
 | 0.83349 | 0.96431 | 0.32338
 | 0.85409 | 0.88251 | 0.2295
 | 0.81009 | 0.84031 | 0.45791
MEAN | 0.8491 | 0.9126 | 0.3210
STD | 0.0459 | 0.0477 | 0.1419
MIN/MAX | 0.75579/ 0.91288 | 0.84031/ 0.99365 | 0.13195/ 0.61523
Segmentation
3D Mesh
Segmentation
Segmentation
Segmentation
3D Mesh
3D Mesh
3D Mesh
Trachea
Liver
Pancreas
Kidney
(1)
(2)
(3)
(3)
(4)
(4)
(4)
(4)